## Slide 1: Binary Numbers
Computer Addressing

## Slide 3: Number Systems Used in Computers
Decimal System (Base 10)
  Digits: 0,1,2,3,4,5,6,7,8,9
  Used for communicating with human users
Binary System (Base 2)
  Digits: 0,1 (On or Off)
  Binary 10 == Decimal 2
  Used by internal CPU and Memory circuits
Octal System (Base 8)
  Digits: 0,1,2,3,4,5,6,7 (No digits 8 & 9)
  Octal 10 == Decimal 8
  Used by Computer Scientists for groupings of 3 binary digits
Hexadecimal System (Base 16)
  Digits: 0,1,2,3,4,5,6,7,8,9, A, B, C, D, E, F (Uses extra letters)
  Hex F == Decimal 15
  Hex 10 == Decimal 16
  Used by Computer Scientists for groupings of 4 binary digits

## Slide 4: Decimal vs. Binary System
Decimal System
Uses Digits:
  0, 1, 2, 3, 4, 5, 6, 7 , 8, 9
Addition
  0 + 1 = 1
  1 + 1 = 2
  99 + 1 = 100
Powers of 10
  100 = 1
  101 = 10
  102 = 100
  Etc.
Evaluate 111
  111 = 102 + 101 + 100
  (100 + 10 + 1)
Binary System
Uses Digits:
  0, 1 (True, False) (+, -)
Addition
  0 + 1 = 1
  1 + 1 = 10
  11 + 1 = 100
Powers of 2
  20 = 1
  21 = 10 (or 2 decimal)
  22 = 100 (or 4 decimal)
  Etc.
Evaluate 111
  111 = 22 + 21 + 20
  (Decimal : 4 + 2 + 1 = 7)
Definition: 1 Bit = 1 Binary Digit

## Slide 5: Base 10
Evaluate 111
In Decimal
 | 100 | 102 | 100
+ | 10 | 101 | + 10
+ | 1 | 100 | + 1
= | 111 |  | = 111

## Slide 6: Base 2
Evaluate 111
In Binary
 | 100 | 22 | 4
+ | 10 | 21 | + 2
+ | 1 | 20 | + 1
= | 111 |  | = 7

## Slide 7
Power of 2 | Decimal Value | Integer Range | Number of Bits | Computer Binary
21 | 2 | 0 - 1 | 1 | 0001
22 | 4 | 0 - 3 | 2 | 0011
23 |  |  |  | 0111
24 |  |  |  | 1111
25 |  |  |  | 0001 1111
26 |  |  |  | 0011 1111
27 |  |  |  | 0111 1111
28 | 256 | 0 - 255 | 8 | 1111 1111
29 |  |  |  | 0001 1111 1111
210 |  |  |  | 0011 1111 1111
211 |  |  |  | 0111 1111 1111
212 |  |  |  | 1111 1111 1111
213 |  |  |  | 0001 1111 1111 1111
214 |  |  |  | 0011 1111 1111 1111
215 |  |  |  | 0111 1111 1111 1111
216 | 65,535 | 0 – 65,534 | 16 | 1111 1111 1111 1111

## Slide 8
Power of 2 | Decimal Value | Integer Range | Number of Bits | Computer Binary
21 | 2 | 0 - 1 | 1 | 0001
22 | 4 | 0 - 3 | 2 | 0011
23 | 8 | 0 - 7 | 3 | 0111
24 | 16 | 0 - 15 | 4 | 1111
25 | 32 | 0 - 31 | 5 | 0001 1111
26 | 64 |  | 6 | 0011 1111
27 | 128 |  | 7 | 0111 1111
28 | 256 | 0 - 255 | 8 | 1111 1111
29 | 512 |  |  | 0001 1111 1111
210 | 1024 |  |  | 0011 1111 1111
211 | 2048 |  |  | 0111 1111 1111
212 | 4096 |  |  | 1111 1111 1111
213 | 8192 |  |  | 0001 1111 1111 1111
214 | 16384 |  |  | 0011 1111 1111 1111
215 | 32768 |  |  | 0111 1111 1111 1111
216 | 65,536 | 0 – 65,535 | 16 | 1111 1111 1111 1111

## Slide 9: Binary Conversions
Convert the following binary numbers to decimal:
11 binary =
101 binary =
1010 binary =
Convert the following decimal numbers to binary:
6 decimal =
13 decimal =

## Slide 10: Binary Conversions
Convert the following binary numbers to decimal:
11 binary = 3 decimal (i.e. 2 + 1)
101 binary = 5 decimal (i.e. 4 + 1)
1010 binary = 10 decimal (i.e. 8 + 2)
Convert the following decimal numbers to binary:
6 decimal = 110 binary (i.e. 4 + 2)
13 decimal = 1101 binary (i.e. 8 + 4 + 1)

## Slide 11: Binary Addition
Add the following binary numbers (verify your answers using decimal)
a) | 0101 | (decimal 5) |  | b) | 0101 | (decimal 5)
 | + 0010 | (decimal 2) |  |  | + 1010 | (decimal 10)
c) | 0011 | (decimal 3) |  | d) | 0110 | (decimal 6)
 | + 0010 | (decimal 2) |  |  | + 0011 | (decimal 3)

## Slide 12: Binary Addition
Add the following binary numbers (verify your answers using decimal)
a) | 0101 | (decimal 5) |  | b) | 0101 | (decimal 5)
 | + 0010 | (decimal 2) |  |  | + 1010 | (decimal 10)
 | 0111 |  |  |  | 1111 | 
c) | 0011 | (decimal 3) |  | d) | 0110 | (decimal 6)
 | + 0010 | (decimal 2) |  |  | + 0011 | (decimal 3)
 | 0101 |  |  |  | 1001 | 

## Slide 13: Computer Memory

## Slide 15: Prefixes
Kilo (K) means __________________ Multiply by x______________
Mega (M) means _________________ Multiply by x______________
Giga (G) means __________________ Multiply by x______________
Tera (T) means __________________ Multiply by x______________

## Slide 16: Prefixes
Kilo (K) means ___Thousand_______ Multiply by x__1,000_______
Mega (M) means __Million________ Multiply by x__1,000,000___
Giga (G) means ___Billion________ Multiply by x __1,000,000,000___
Tera (T) means ___Trillion________ Multiply by x __1,000,000,000,000___

## Slide 17: Examples
64 Mbps (Mega-bits per seconds) = ________________ bps (bits per second)
256 Giga-bytes = ________________ bytes
256 Giga-bytes = ________________ bits

## Slide 18: Examples
64 Mbps (Mega-bits per seconds) = __64,000,000______ bps (bits per second)
256 Giga-bytes = __256,000,000,000___ bytes
256 Giga-bytes = __2,048,000,000,000___ bits

## Slide 19: Computer Memory Structures
Bit
  1 binary digit
  Used for Boolean data type
  Building Block for All computer data and memory
Byte
  8 binary digits
  Largest value: 1111 1111 (28 – 1 = 255 Decimal)
  Used for Char (character) data type
    26 lower case letters + 26 uppercase letters + 10 number symbols + punctuation marks+ Other Stuff equal about 130 distinct characters

## Slide 20: Computer Memory Structures
Word
  16 binary digits (2 bytes)
  Largest value: 1111 1111 1111 1111 (216 – 1 = 65,535 Decimal)
Integer data type (Short)
  Is 1 Word (16 bits)
  But must represent both Positive (+) and Negative (-)
  Range: +32767 to -32768
  Larger or smaller numbers require a different data type

## Slide 21: Computer Memory Structures
Double Word
  32 binary digits (4 bytes or 2 words)
  Largest value: 232 – 1 = 4 billion approx)
Integer data type (Long)
  Provides much larger range than Integer for Positive (+) and Negative (-) numbers
Double Word Memory Addressing
  Provides access to about 4 GB of memory max.

## Slide 23: Research Questions
6 Questions
Download from GitHub
Answer & Upload

## Slide 24: ASCII Character Codes